## Slide 1: Global Internet

## Slide 2: Where Are We?
Internet
  Connect heterogeneous collection of networks
  Simple addressing hierarchy
Scalability Challenges
  Several challenges exist to make the Internet of global scale
  We address several of these in these notes.

## Slide 3: Global Internet – Summary of Topics
IP address hierarchy evolution
  Subnetting
  CIDR
Evolution of Internet structure
Virtual geographies
  Networks
  Domains (Autonomous Systems)
Routing with domains
  Intradomain routing
  Interdomain routing

## Slide 4: Problems of Scale
Inefficient address allocation
  Most physical networks (i.e. LANs) have only about 100 hosts or less
  Assigning class A or B to them would be wasteful.
  Solution: subnetting
Too many networks for routing
  Networks at the core need to be “aware” of each class A, B, and C network number
  Too many networks! Routing tables don’t scale
  Solution: CIDR
We will tackle each of these in turn (i.e. we start with 1 above)

## Slide 5: Subnetting
Assume an organization is given a class B network #
  Class B has two bytes for network # and two bytes for the host #
  E.g., 128.174.0.0 (recall, network #’s have 0’s for the host bits)
Think of this as an “address block” of 2^16 addresses
First address in the block is 128.174.0.0
Last address in the block is 128.174.255.255
Actually, 2^16 – 2 addresses (128.174.0.0 and 128.174.255.255 cannot be used  )
I sometimes draw this block as follows
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 6: Subnetting continued …
Assume the organization has multiple physical networks with a few hundred hosts in each physical network.
The class B network # can be broken into smaller “sub”networks
Idea: take a single IP network number
  Break its block of addresses into smaller blocks (subnets).
  Allocate a smaller block of IP addresses to each physical network.
  Not all blocks are of the same size!

## Slide 7: Example
Consider again network 128.174.0.0
One sub-block of addresses could be as follows:
First 25 bits identify the network and the subnetwork
The last 7 bits identify the host within the subnetwork
This subnetwork is identified as 128.174.142.128 (zero for the host bits).
It also has associated with it a subnet “mask” 1 – network or subnet bit, 0 – host bit
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
X
X
X
X
1
0
0
0
1
1
1
0
1
X
X
X
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
1
0
0
0

## Slide 8: Another subnet
Consider again network 128.174.0.0
Another sub-block of addresses could be as follows:
First 24 bits identify the network and the subnetwork
The last 8 bits identify the host within the subnetwork
This subnetwork is identified as 128.174.141.0 (zero for the host bits).
It also has associated with it a subnet “mask” 1 – network or subnet bit, 0 – host bit
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
X
X
X
X
1
0
0
0
1
1
0
1
X
X
X
X
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0

## Slide 9: Why a subnet mask?
Assume I tell you about a subnet number:
  128.174.141.0
How many bits are for the network/subnet and how many bits are for the host? Can you tell?
Routing table entries within the organization include the subnet number AND its associated subnet mask

## Slide 10: Subnetting – in summary
Assumptions
  Subnets are close together (same company)
    Looks like a single network to routers outside the organization
    Hence, outside routers only have a single entry in their table for the organization.
IP with Subnetting:
  All hosts in the same company have the same network#
  All hosts on the same physical network must have the same subnet # (an “extension” of network #)

## Slide 11: Subnetting Example
H1
H2
H3
R1
R2
Subnet Mask: 255.255.255.128 (last byte, bin 1000 0000)
Subnet Number: 128.174.142.128 (last byte, bin 1000 0000)
Subnet Mask: 255.255.255.0
Subnet Number: 128.174.141.0
Subnet Mask: 255.255.255.128 (last byte, bin 1000 0000)
Subnet Number: 128.174.142.0 (last byte, bin 0000 0000)
128.174.142.200
128.174.141.3
128.174.142.27
Note: subnet masks are not of the same length
Can we replace the subnet mask of 128.174.142.0 by 255.255.255.0?
Can we have an additional subnet 128.174.142.0 with mask 255.255.255.0?
Can we have an additional subnet 128.174.140.0? How many bits can we have in the mask?

## Slide 12: Subnetting (host IP XOR SM = SN #)
Subnet # 128.174.141.0
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
0
0
0
0
1
0
0
0
1
1
0
1
0
0
0
0
Subnet Mask 255.255.255.0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
0
0
0
0
Host 3: 128.174.141.3
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
0
0
1
1
1
0
0
0
1
1
0
1
0
0
0
0
Subnet # 128.174.142.128
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
0
0
0
0
1
0
0
0
1
1
1
0
1
0
0
0
Subnet Mask 255.255.255.128
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
1
1
0
0
0
Host 1: 128.174.142.200
1
1
1
0
1
0
0
0
0
0
0
0
1
0
1
0
1
0
0
0
1
0
0
0
1
1
1
0
1
1
0
0

## Slide 13: Subnetting
H1
H2
H3
R1
R2
Subnet Mask: 255.255.255.128
Subnet Number: 128.174.142.128
Subnet Mask: 255.255.255.0
Subnet Number: 128.174.141.0
Subnet Mask: 255.255.255.128
Subnet Number: 128.174.142.0
128.174.142.200
128.174.141.3
128.174.142.27
Send an IP packet from H1 to H3: send directly or via a router?
At H1:
Compute (H3 “subnet number”)
  128.174.141.3 AND 255.255.255.128 = 128.174.141.0 ( 128.174.142.128 = H1’s subnet #)
If result = H1’s subnet number
  then H3 and H1 are on the same subnet
Else
  route through appropriate router

## Slide 14: Subnetting
Example Table from R2
  Next hop (AND against subnet mask, compare to subnet #)
    128.174.142.196 to R1 (why not R3?)
    128.174.142.95 to Interface 1
    128.174.141.137 to Interface 0
    129.174.145.18 to R3
    131.126.244.15 to R3
Subnet # | Subnet Mask | Next Hop
128.174.141.0 | 255.255.255.0 | Interface 0
128.174.142.0 | 255.255.255.128 | Interface 1
128.174.142.128 | 255.255.255.128 | R1
128.174.0.0 | 255.255.0.0 | R3
0 (Default) | 0.0.0.0 | R3

## Slide 15: Subnetting
Notes
  Non-contiguous subnets are difficult to administer
  Multiple subnets on one physical network
    Must be routed through router
Pros
  Helps address consumption
    Better use of class A and B addresses
  Helps reduce routing table size of routers outside the organization
    one network # per company rather than multiple network numbers per company (one per physical network)

## Slide 16: Problems of Scale: need for CIDR
Most companies plan to have more than 255 machines (Class C)
  Thus they choose a class B
  Otherwise, renumbering is time consuming and can interrupt service.
Class B networks aren’t very efficient
  Approximately 16,000 class B networks available
  Few organizations have O(10,000) machines
    More likely use O(1,000) of the 65,000 addresses
What about multiple class C networks per company?
  Routing tables in the core don’t scale in this case (too many networks)
  Protocols do not scale beyond O(10,000) networks

## Slide 17: Solution – Classless Interdomain Routing (CIDR)
Eliminate class notation (A, B, and C are gone!)
Generalize subnet notion and subnet masks (just mask).
Allow only contiguous masks
Specify network by (network no. / no. of bits in mask)
The mask is dynamic
  Think of a network as a “region” where all machines have the same prefix (network number) in their IP address.
  As you get closer to the destination, the mask size (prefix length) “increases”, I.e. more details are available.
Aggregate routes in routing tables – contiguous blocks of network numbers along the same path are aggregated into one network with a shorter mask (prefix length)

## Slide 18: Starting from the bottom 
Organization X was given a “class C” address block 192.4.16.0/24
But a physical network in the org. has only 6 hosts
Thus, for this phys. netw., X uses 3 bits for the host (29 for netw #)
  192.4.16.0/29
Remaining addresses may be given to other physical networks
192.4.16.0/24 Class C address block given to organization X
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
x
x
x
x
0
0
0
1
0
0
0
0
x
x
x
x
24 bits identify the class C network
192.4.16.0/29 Network number of small physical network
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
x
x
x
0
0
0
1
0
0
0
0
0
0
0
0
29 bits identify the physical network

## Slide 19: Further Aggregation
Assume organization X is given a block of 16 contiguous C netw numbers.
  E.g. 192.4.16.0/24 – 192.4.31.0/24 (see picture below)
Organization X is identified by 192.4.16.0/20, where network number 192.4.16.0, and prefix length (mask) is 20 bits.
Routers outside the organization have one entry, rather than 16 entries
Block size (# of addresses) must be a power of 2
Network number may be any number of bits
192.4.31.0/24 Last class C network #
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
X
X
X
X
0
0
0
1
1
1
1
1
X
X
X
X
192.4.16.0/24 First class C network #
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
X
X
X
X
0
0
0
1
0
0
0
0
X
X
X
X
192.4.16.0/20 X’s block of addresses
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
X
X
X
X
0
0
0
1
X
X
X
X
X
X
X
X
20 bits identify the organization X

## Slide 20: Even More Aggregation
A service provider could be assigned the network address 192.4.0.0/16
It further breaks this address into contiguous blocks of addresses and gives them to its client organizations.
One of them is 192.4.16.0/20 for organization X as before.
Routers outside the service provider have only a single entry for the entire service provider, I.e., 192.4.0.0/16
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
Organization X: 192.4.16.0/20
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
Organization Y: 192.4.128.0/17
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Service Provider: 192.4.0.0/16
20 bits identify the organization X
16 bits identify the service provider
17 bits identify the organization Y

## Slide 21: Routing with CIDR
Core routers will only care about the first 16 bits of 192.4.0.0/16 to reach the service provider
Service provider routers care about the first 20 bits in 192.4.16.0/20 to reach organization X
  X cares about the first 29 bits in 192.4.16.0/29 to reach the specific physical network (Ethernet)

## Slide 22: Longest Match Prefix (weird)
Assume a service provider P has a contiguous group of addresses.
This group was split into different organizations, X, Y, Z, etc.
What if X changes to service provider Q? Its IP addresses would change (bad, lots of renumbering)
X is allowed to keep its IP addresses.
P advertises to outside routers that it can reach the contiguous group of addresses (including X!)
Q advertises the more specific group of addresses of X.
Routers must follow path to Q, since Q has more “specific” information (longest prefix).

## Slide 23: CIDR
Trend is for increasing amounts of overlap in routing table entries
Example: 128.174.142.200
  Matches second, third and fourth lines
  Route to entry with longest match (always!)
Subnet # / length | Next Hop
128.174.141.0 / 24 | Interface 0
128.174.142.192 / 27 | Interface 1
128.174.142.128 / 25 | R1
128.174.0.0 / 16 | R3
Default | R3

## Slide 24: Need for More Scalability
Even with CIDR, it is not scalable enough
For a routing protocol to work, all routers in a network are aware of all other routers in the network
My router here in UTD should not need to know about or talk to routers in Hong Kong.
We need to break the Internet into pieces, or “routing domains”

## Slide 25: Autonomous Systems (Routing Domains)
The Internet is subdivided into Autonomous Systems
There are currently about 13000 active ASM’s
Based on notion of autonomy of control
E.g.: company, university, etc
Each AS has a unique 16 bit ID

## Slide 26: AS Picture and meta picture
Enables hierarchical aggregation of routing information
An entire AS may be viewed as a single “node”
A “meta” routing protocol finds paths from one AS to another
R1
Autonomous system 1
R2
R3
Autonomous system 2
R4
R5
R6
R7
Autonomous system 3
R8
R9
R10
AS1
AS2
AS3

## Slide 27: Autonomous Systems
Intradomain Routing (within an AS)
  Performed using domain-specific algorithm (e.g. OSPF, RIP)
  Selected by domain administrators
  Allows heterogeneous interior gateway protocols
Interdomain Routing (between ASM’s)
  Performed using standard global algorithm
  Nodes in the routing table are AS’s
  Homogeneous exterior gateway protocol (why?)
  Main goal: reachability

## Slide 28: Standard Interdomain Routing Protocols
General aspects
  Very complex and difficult
  Large scale (140,000 network prefixes in the core of the network, and about 14,000 AS numbers)
  Focuses on reachability rather than optimality
  Must be loop-free
  Specify how reachability information should be exchanged

## Slide 29: Old Tree-Structure
Internet before 1990 had a tree-structure
Main “core” was the NSF Backbone (NSFNET)
An AS could have a parent and/or children
No “peering”, strictly hierarchical.
A low level AS could have a default route to its parent (and thus need not know the whole Internet).
However, the NSFNET needed to know the whole Internet
NSFNET backbone
Stanford
BARRNET
regional
Berkeley
P
ARC
NCAR
UA
UNM
W
estnet
regional
UNL
KU
ISU
MidNet
regional
…

## Slide 30: EGP (OLD)
Defined on the Internet having a tree structure
Embodied (and enforced) tree structure
Each AS must learn how to reach every AS in its sub-tree
Thus, the core network learns the path to every AS
Distance vector updates
Had to be replaced eventually

## Slide 31: Privatization of the Internet
Backbone service provider
Peering
point
Peering
point
Large corporation
Large corporation
Small
corporation
“
Consumer
”
ISP
“Consumer” ISP
“Consumer” ISP
Mid 1990’s, NSF relinquished control of the Internet backbone
We have many commercial backbone providers (UUNet/Worldcomm, Sprint, MCI, ...)
Mesh connectivity, multi-homed networks,
Loops galore
Need a new solution

## Slide 32: Types of AS
Stub: only connected to one other AS; carries local traffic only (can use default path to its parent AS, and does not necessarily have an AS number)
Multi-homed: connected to multiple ASM’s, but refuses to carry transit traffic
Transit: allows traffic from other ASM’s to cross it.
Need a protocol that can handle this general connectivity

## Slide 33: Reachability vs Optimality
Each domain can choose its own interior routing protocol (intradomain)
It can choose any scheme to assign metrics (i.e. costs) to its interior paths
No consistency between ASM’s
  Value of 1000 in one AS may be great, but awful at another
Impossible to find the least cost path to a destination AS.
Best you can do is find “a path”.
Each AS advertises “reachability information”
  I can reach AS n and it contains networks 129.18.0.0/16 and 100.18.0.0/16
  No cost is given.

## Slide 34: Loop Freedom (must avoid loops)
Short-lived or long-lived routing loops are devastating
  The traffic of an entire AS could be interrupted
  Looping packets would cause congestion
Example
  AS2 announces to AS3 it can reach AS0
  AS3 announces to AS4 it can reach AS0
  AS4 announces to AS2 it can reach AS0
  AS2 chooses AS4 as its next hop to AS0
AS1
AS2
AS3
AS4
AS0

## Slide 35: Need for Flexible Routing Policies
We could choose the path with least # of AS-hops
However, other factors may be more important:
  An AS may prefer a neighboring AS according to:
    Some economic relationship
    Level of trust (may not trust some ASM’s)
  Also, each AS is not forced to disclose its reachability
    Multi-homed ASM’s prevent through traffic by not announcing reachability
Thus, domains should have the freedom to choose their path to each destination domain (flexible routing policy)
The whole point is to find a “good” path not an optimal one.

## Slide 36: Review: intradomain routing protocols
Common intradomain routing protocols
  Routing Information Protocol (RIP)
    From the early Internet
    Part of Berkeley Software Distribution (BSD) Unix
    Distance vector algorithm
    Based on hop count (infinity set to 16 hops)
  Open Shortest Path First (OSPF)
    Internet Standard (RFC 2328)
    Link state algorithm
    Authenticates messages
    Load balances across links

## Slide 37: Why not DV or Link-State for interdomain routing?
Link-State
  Too much overhead O(N2) message and processing overhead.
  Even for intradomain routing it has too much overhead
Distance Vector
  Slow to converge (counting to infinity)
    We may choose all links to have a cost of “1”, but short-lived loops still would exist
Need for flexible policies
  Neither of the above two supports flexible policies, because the entire path information is needed.
  Both of the above look for min-cost paths, not flexible enough to implement routing policies.

## Slide 38: BGP-4
Current standard interdomain routing protocol
Assumption
  Internet is an arbitrarily interconnected set of AS’s
Traffic
  Local: Begins or ends within an AS
  Transit: Moves through an AS
Each AS has
  Border routers (one or more)
    Connects an AS to the Internet
    Used for default external route
  BGP speakers (one or more)
    Routers that participate in the interdomain routing protocol

## Slide 39: BGP-4
Neither link-state nor distance-vector
BGP speakers advertise, for each network N,
  The full path (list) of ASM’s to reach network N
Loops are avoided by not choosing a neighbor’s path if it contains your own AS ID.
Only one path is advertised even if many are available.
  Advertise the route that you have chosen according to your routing policies.

## Slide 40: BGP-4 path advertisements
Example
  AS10 advertises 131.141/16 and 192.10.20/24 as local networks
  AS6 advertises same networks with path (AS6, AS10)
  AS19 advertises same networks with path (AS19, AS6, AS10)
AS10
AS18
AS19
AS6
131.141/16
192.10.20/24

## Slide 41: TCP Connectivity
Neighboring (peer) BGP speakers connect to each other using TCP (reliable)
Information is not “refreshed”
Only “keep-alive” messages are sent periodically to each neighbor.
Advertised paths, if no longer existent, must be withdrawn explicitly.
  Thus, a router has two explicitly tell its neighbors a path is no longer available.

## Slide 42: Multiple BGP Speakers per AS
Two types of neighbors
  Internal: in the same AS, use iBGP protocol
  External: in a different AS, use eBGP protocol
Full TCP connectivity with internal neighbors.
  All internal neighbors share the routes they learned from outside ASM’s.
  Internal neighbors may be multiple hops away!

## Slide 43: Why is everything more scalable?
Two levels of the hierarchy
  Outside of an AS (interdomain)
  Within an AS (intradomain)
Interdomain: Finding the next-hop AS and its border router is scalable: there are less ASms than networks.
Intradomain: Within an AS you must find a path to the border router (done by, e.g., OSPF protocol)

## Slide 44: Integrating Interdomain and Intradomain
Customer AS: how to reach the outside world?
  It is a stub AS
  Assume only the border router speaks BGP (interior routers do not)
  How do non-BGP speakers in AS10 learn how to reach the Internet?
  The border router “injects” a default path into the intradomain protocol (e.g. OSPF or RIP)
  All traffic from customer is sent via the border router to the service provider
AS10
AS18
AS19
AS6
Customer
Service Provider
Backbone Network
131.141/16
192.10.20/24
128.140/16
182.10/16

## Slide 45: Integrating Interdomain and Intradomain
Service Provider AS6: how to reach customer? (from non-BGP routers inside AS6)
  The AS6 router bordering with AS10 “injects” into its intradomain protocol that it has a “link” of cost X to networks 131.141/16 and 192.10.20/24
  The AS6 router bordering with AS18 “injects” into its intradomain protocol that it has a “link” of cost X to networks 128.140/16 and 182.10/216
  Any non-BGP-Speaker router insider the service provider will reach these networks via the border routers.
AS10
AS18
AS19
AS6
131.141/16
192.10.20/24
Customer
Service Provider
Backbone Network
128.140/16
182.10/16

## Slide 46: Integrating Interdomain and Intradomain
Backbone networks: how to reach customer
  Too many prefixes to inject into intradomain protocol
  All routers speak BGP
  Via the iBGP protocol, they share their reachability information (the networks and their AS path to get to them)
  To reach a specific network, iBGP says which border router is needed, and the intradomain protocol gives the next hop to this router.
AS10
AS18
AS19
AS6
Customer
Service Provider
Backbone Network
128.140/16
182.10/16
131.141/16
192.10.20/24

## Slide 47: Problems with BGP
Instability
  Route flapping
  Arbitrary path decisions can lead to route flapping
  Not guaranteed to converge
Over 100,000 network prefixes in some routers (without using defaults)